## Slide 1: Gremlins’ the Sequel – the Horrors of Exascale
LLNL-PRES-xxxxxx
Judit Gimenez, BSC
Martin Schulz, LLNL
http://scalability.llnl.gov/
http://www.bsc.es/

## Slide 2: How (not) to Build an Exascale Machine
Can we make a Petascale class machine behave like what we expect Exascale machines to look like?
  Limit Resources (power, memory, network, I/O, …)
  Increase compute/bandwidth ratios
  Increase fault rates and lower MTBF rates
In short: release GREMLINs into a petascale machine
Goal: Emulation Platform for the Co-Design process
  Evaluate proxy-apps and compare to baseline
  Determine bounds of behaviors proxy apps can tolerate
  Drive changes in proxy apps to counter-act exascale properties

## Slide 3: How to Release GREMLINs onto your Machine
Techniques to force “bad” behavior on “good” systems
  Target individual resources and artificially limit them
    Using hardware techniques
    Stealing resources by creating contention
  Directly inject bad behavior through external events
Individual GREMLINs are implemented as modules
  One effect at a time
  Orthogonal to each other
  Each GREMLIN has “knobs” to control behavior
The GREMLIN framework
  Dynamic configuration and loading of individual GREMLINs
  Ability to couple a range of “bad behaviors”
  Transparent to system and (mostly) to applications

## Slide 4: The Gremlin Architecture
Applications
Architecture
Applications
Architecture
Measurement
Measurement
Measurement
GREMLIN Env.
GREMLIN Env.
GREMLIN Env.
Power GREMLIN
Fault GREMLIN
Applications
Architecture
Rank 0
Rank 1
Rank N
Multi node job (e.g., MPI)
Front end node
GREMLIN
Control
Power GREMLIN
Memory GREMLIN

## Slide 5: Broad Classes of GREMLINs
Power
  Impact of changes in frequency/voltage
  Impact of limits in available power per machine/rack/node/core
Memory
  Restrictions in bandwidth
  Reduction of cache size
  Limitations of memory size
Resiliency
  Injection of faults to understand impact of faults
  Notification of “fake” faults to test recovery
Noise
  Injection of controlled or random noise events
  Crosscut summarizing the effects of previous GREMLINs

## Slide 6: Broad Classes of GREMLINs
Power
  Impact of changes in frequency/voltage
  Impact of limits in available power per machine/rack/node/core
Memory
  Restrictions in bandwidth
  Reduction of cache size
  Limitations of memory size
Resiliency
  Injection of faults to understand impact of faults
  Notification of “fake” faults to test recovery
Noise
  Injection of controlled or random noise events
  Crosscut summarizing the effects of previous GREMLINs

## Slide 7: Results from the Power Gremlins
Using RAPL to install power caps
  Exposes chip variations
  Turns homogenous machines into inhomogeneous ones
Optimal configuration under a power cap
  Widely differing performance
  Application specific characteristics
  Need for models

## Slide 8: Update on Power Gremlin Infrastructure
Low-level infrastructure
  Libmsr: user-level API to enable access to MSRs (incl. RAPL capping)
  Msr-safe: kernel module to make MSR access “safe”
Current status
  Support for Intel Sandy Bridge
  More CPUs (incl. AMD) in progress
  Code released on github: https://github.com/scalability-llnl/libmsr
  Inclusion into RHEL pending
  Deployed on TLCC cluster cab
Analysis update
  Full system characterization (see Barry’s talk)
  Application analysis in progress

## Slide 9: Next Steps: Feeding the Gremlins After Midnight
Scheduling research
  Find optimal configurations for each code
  Balance processor inhomogeneity
  Understand relationship to load balancing
  Integration into FLUX
New Gremlins
  Artificially introduce noise events
  Network Gremlins
    Limit network bandwidth or increase latency
    Inject controlled cross traffic
Adaptation of the Gremlins to new programming models
  Initially developed for MPI (using PnMPI as base)
  First new target: OmpSs

## Slide 10: BSC Experiments with Gremlins
Gremlins integrated with
  OmpSs runtime
  Extrae instrumentation (online mode)
Analysis of Gremlins’ impact
  Living with Gremlins! Measure applications’ sensitivity
  Growing our Gremlins! uniform vs. non-uniform populations
  Have Gremlins side-effects?
    Do they increase/affect variability?
    Should not affect other resources
First results
  Up to now playing with memory Gremlins

## Slide 11: Integrating Gremlins in OmpSs runtime system
Gremlins launched at runtime initialization but remain transparent
Each gremlin thread is exclusively pinned on one core
These processors then become inaccessible by the runtime
Runtime parameters can be used to
  enable/disable gremlins,
  define number of gremlin threads, resource type
  how much of that resource a single gremlin thread should use
Marc Casas

## Slide 12: Current Work
Identify sensitive tasks
  Classify how sensitive they are
  Match them with tasks that can be run concurrently and are less sensitive to the respective resource type
Implement smart Scheduler in OmpSs
  Modify OmpSs scheduler to identify resource sensitive tasks with the use of gremlin threads
  Implement a scheduler that takes this information into account when scheduling tasks for execution

## Slide 13: Results L3 cache capacity interference
0 gremlin - 20MB
1 gremlin - 15MB
2 gremlin - 12MB
3 gremlin - 7MB
4 gremlin - 4MB

## Slide 14: Results with memory BW interference
0 gremlin - 40GB/s
1 gremlin - 37.2GB/s
2 gremlin - 34.3GB/s
3 gremlin - 31.5GB/s
4 gremlin - 28.7GB/s

## Slide 15: CGPOP sensitivity LLC cache size and bw
Without gremlins
Limiting size (4MB)
Limiting bandwidth (28.7 GB/s)

## Slide 16: CGPOP sensitivity LLC cache – variability / unbalance
4lnj8dmatvec
8hyn9lpcg
Limiting size (4MB)
Limiting bandwidth (28.7 GB/s)

## Slide 17: CGPOP sensitivity LLC cache – unbalance along time
8hyn9lpcg
Limiting size (4MB)
Limiting bandwidth (28.7 GB/s)

## Slide 18: CGPOP sensitivity LLC cache – tracking evolution
4lnj8dmatvec
8hyn9lpcg
ahyn9lpcg
3hyn9lpcg
Limiting bandwidth

## Slide 19: Integrating Gremlins in Extrae
Extrae online analysis mode
  Based on MRNet
Gremlins API to activate them locally
  All Gremlins launched at initialization time
First experiments with LLC cache size gremlins
  Periodic increase of Gremlins
  Unbalanced steal of resources

## Slide 20: LULESH sensitivity to LLC cache size
Can we extract insight from chaos?
  Unbalanced Gremlins creation

## Slide 21: LULESH sensitivity to LLC cache size – tracking evol.
L3/instr. ratio

## Slide 22: Conclusions
Different regions show different sensitivity to resource reductions
Asynchrony affects actual sharing of resources
  Today happens without control  variability
Detailed analysis detects increases on variability and potential non-uniform impact